## Slide 1: Next Generation Wi-Fi VoIP phones
Dr.-Ing. Christian Hoene
Universität Tübingen
IQPC Conference VoWLAN
Berlin, 5th July 2006

## Slide 2: Content: First Part
State of the Art
Comparing VoWLAN, GSM, and DECT
Disruptive Technology
Location-based Services with WLAN
New Codecs beyond Narrow-Band Voice
Efficient Internet Codecs
Summary

## Slide 3: Where are we now?
Phy: IEEE 802.11b/g
MAC: WMM or WME for QoS
Security WEP-WPA2
Network: IPv4
Transport and Signaling: RTP, SIPv2
Codecs: G.711, 723, 726 and G.729a/b
Acoustics: Comfort noise generation (CNG), voice activity detection (VAD), adaptive jitter buffer and echo cancellation
Battery life: With 800mA battery-Four hours talk time-Sixty hours stand-by time

## Slide 4: Comparing VoWLAN with GSM and DECT Phones
GSM technology is used for cellular networks
  e.g. a recent Nokia GSM/UMTS phone
  Weight 117g
  Battery: BL-5C Li-Ion (970mAh)
  Standby time: 144 - 288 h
  Talk time: 3,3 - 6,4 h
  Transmission range: up to 35 km
  Price: 340 €
DECT technology is used for cordless phones
  e.g. Siemens Gigaset S44
  Weight 120g
  Battery: NiMH AAA (750 mAh)
  Standby time: up to 150h
  Talk time: up to 10h
  Range: up to 300 m
  Transmission Range: 50 m (indoor) and 300 m (outdoor)
  Price: 70 €
Is VoWLAN a better technology than GSM or DECT?

## Slide 5: Operating Times of VoWLAN Phones
Nokia E60
UTStarcom F3000 Zyxel ePhone P2000W
UTSTarcom F1000G

## Slide 6: Operating Times of a GSM Phone
Nokia E60
UTStarcom F3000 Zyxel ePhone P2000W
UTSTarcom F1000G
Nokia E60 GSM Mode

## Slide 7: Operating Times of a DECT Phone – even better
Nokia E60
UTStarcom F3000 Zyxel ePhone P2000W
UTSTarcom F1000G
Siemens
Gigaset
S44
Nokia E60 GSM Mode

## Slide 8: Comparing VoWLAN, GSM, vs. DECT
VoWLAN has
  Lower range than GSM
  Higher power consumption than DECT/GSM
  Lower standby times than DECT/GSM
  Lower times than DECT/GSM
  Higher prices than DECT
Is VoWLAN any good at all?
  Why are we here at this conferences?
VoWLAN
  is based upon Internet (IP)
  Is a young technology and will enhance
  Has other qualities than talk times, standby times, energy consumption
VoWLAN is a disruptive technology.

## Slide 9: Disruptive Technology
Term defined by C. M. Christensen in “The Innovator's Dilemma”:
“A disruptive technology is a new technological innovation, product, or service that eventually overturns the existing dominant technology or product in the market. Disruptive technology is radically different from the existing technology and is often not as good as the established technology, in terms of expectations of most profitable customers. But a disruptive techno-logy or innovation is simple, inexpensive, and convenient to use.
Low-end disruption … targets customers who do not need the full performance.
New-market disruption targets customers who could previously not be served profitably by the incumbent. “
[http://en.wikipedia.org/wiki/Disruptive_technology]

## Slide 10: VoWLAN is a Disruptive Technology
VoWLAN is a low-end disruption
  Quality is good enough
  Similar to typical wireless phones a few years ago
VoWLAN is a new-market disruption
  enables new features
  has other qualities
But VoWLAN has to evolve:
  New features in addition to speech communication e.g. location based services
  Simple charging and roaming
  Better speech coding beyond narrow-band voice
  Efficient Internet codecs

## Slide 11: Ad 1: Location Based Services
VoIP needs location based services for
  E911 calls.
  Cinema/theater/conference vibration alarm.
  Integrated value added services.

## Slide 12: Ad 1: Current Positioning Solutions
WirelessLAN Location Based Services use
  Outdoors: GPS
  Indoors: received signal strength indication (RSSI)
Problems of RSSI
  Imprecise due to dynamic conditions inside a building
  Signal strength decreases non linear with distance
  Use signal strength maps to relate RSSI to positions
   maps have to be updated when environment changes and are time consuming to generate

## Slide 13: Ad 1: Distance Measurement based on Round Trip Times
Processing time
Round Trip Time (RTT)
Immediate acknowledgements of IEEE 802.11

## Slide 14: Ad 1: Summary
Result
  Accuracy - better than RSSI
  Approach works reliably for three different chipsets
  Firmware update required for stand-alone solution
Advantages over GPS:
  low-cost commercial WLAN hardware, since time-of-flight of a data packet estimated and NOT Time of Arrival (TOA) of pure RF-signals
  No need for precise, synchronized clocks
Advantages over RSSI:
  no time consuming initiation and map generation
  time measurements less prune to errors resulting from changing conditions in WLAN surrounding as compared to signal strength measurements
IEEE 802 group 11u has recently added an interface for this approach

## Slide 15: Ad 2: Charging as Simple as Refueling
Every hotspot has its own charging solution
  Usually based on WWW interface and credit cards
  At least 1000 different solutions for charging
  Why?
Currently, no IETF standard for charging.
  IETF considers it out-of-scope
  Do they assume that Internet usage shall be at no costs?
We need an Internet protocol for charging
  VoWLAN phones do not have a browser
  VoWLAN users cannot enter credit card numbers
  VoWLAN cannot use any arbitrary hotspot
  Charging must be standardized if roaming shall be automatic

## Slide 16: Ad 3: Better Speech Coding beyond Narrow-Band
PSTN supports the transmission of narrow-band voice
  Frequency band 300 – 3400 Hz
Recently, wide-band voice is supported (AMR-WB, iSAC (Skype)…)
  Frequency band 150 – 6200 Hz
Wide-band speech codecs have been available more than 10 years
  But have not been very successful.
  Why? Because wideband does not enable a new market
We need ultra-wide bandwidth coding for music
  Transmit music over telephones with CD quality
  All ring-tone kids will love it
  Currently three low delay codec available: Speex, AAC-LD and AMR-WB+
  But headsets and acoustic processing still has to be optimized

## Slide 17: Ad 4: Efficient Internet Codecs
Current speech codecs have been design for
  PSTN (G.711, G.729, G.723.1, iLBC, iSAC, …)
  Cellular (GSM, AMR, AMR-WB, …)
  Streaming (MP3, AAC, WMF, …)
Internet is different
  Different metric: not bit rate but packet rate
  In VoWLAN the packet rate is the limiting factor (refer to workshop)
  Speech codings have not been optimized for low packet rate
Even worse: Recently research shows
Many speech codecs are not efficient if used in the Internet.

## Slide 18: Ad 4: Importance of VoIP Packets
Losing one Voice-Over-IP frame impairs the perceptual quality in a wide range, depending on
  the frame speech properties
  the encoder/decoder/concealment algorithms
Example: Discontinuous Transmission (DTX)
  Speech frames during silence are less important
  Lower frame rate during silence
Our research results show
  Many speech frames during voice activity are not relevant
  They can be dropped without any notable impact

## Slide 19: Ad 4: Speech Frames – Dropping Strategy
Drop packets in cases of
- Congestion
- Wireless fading
- Saving transmission energy
Best: dropping the unimportant frames first
Worst: dropping the important frames first
Random frames losses
DTX: drop first silent frames, then active frames (randomly)
MOS 1,5
MOS 0,7
MOS 2,2

## Slide 20: Summary
VoWLAN is a disruptive technology
  which will be judged according to new quality metrics
  but is still a young technology, which has to evolve
As a researchers, we see a quite number features to be improved
  Charging
  Coding
  Additional services
Time scope is about 5 year for the next generation phones
VoWLAN will be successful
  not because it is technological advanced
  but because it has benefits that cannot be achieved with GSM or DECT