## Slide 1: Seven Myths about Wi-Fi VoIP A Vision of Next Generation Wi-Fi VoIP Telephones
Christian Hoene
May 13th, 2005
Hotel Sofitel, Paris Bercy

## Slide 2: Content
Introduction
Seven Myths:
  5% loss rate and 150 ms delay.
  Toll quality.
  Coding rate is important.
  Two codecs are enough.
  Telephony is just narrow-band speech.
  Packet loss rate is significant.
  Use signal strength for location based services.
Conclusion

## Slide 3: Introduction
This presentations covers the
  Technical aspects of the
  Transmission of VoIP over WIFI.
  Sorry, no signaling aspects.
Some basic background is required,
  which you probable have learned or
  refreshed during the last days.
We will show: Seven common statements are
  wrong or, at least,
  imprecise.

## Slide 4: 1. Myth
A VoIP call must not have
a loss rate higher than 5%
a network delay of 150 ms or larger (or any other arbitrary set of values)

## Slide 5: Mean Loss Rate vs. Speech Quality [1]
Using 3GPP Adaptive Multi-Rate Coding (AMR)
supports coding rates from 4.75 to 12.2 kbit/s.
Speech quality (MOS)
Poor Fair Good
Mean packet loss rate [%]

## Slide 6: Impact of Delay on Call Quality [2]
NTT (human test results)
ITU E-Model
Bellcore (human test results)

## Slide 7: How to Judge the Quality of a Call?
Measure the quality of a Wifi-Voice system:
Gather packet loss rates, mean delay, etc.
  Easy but inaccurate
In the end the service quality is important
  Human based listening tests are extensive and expensive.
ITU P.862 (PESQ algorithm) measures speech quality
  Compares original sample with the transmitted version
  calculates Mean Option Score (MOS) (1=bad, 5=excellent)
ITU G.107 (E-Model) predicts quality of tel.-system
  Considers echo, loudness, coding, packet loss rate, delay, …
  Result: R Factor (0=bad, 100=excellent)

## Slide 8: Assessing a Trace of VoIP Packets
PESQ and E-Model cannot judge the impact of:
Variable packet delay  adaptive playout time
Packet losses are considered to be random but sometimes depend on the content and context of the speech frame
Not applicable to assess VoIP packets traces resulting from simulations or experiments
Our solution:
Using different playout schedulers and encoding schemes
Combine von E-Model and PESQ [3] (conversation formula approved by the ITU as standard extension)
  PESQ calculate speech quality
  E-Model to combine MOS rating and transmission delays

## Slide 9: Speech Quality and Transmission Delay

## Slide 10: Result
Optimize with human perception in mind.
Packet losses and delays are important,
but have very complex relation to quality.
References:
[1] C. Hoene, H. Karl, and A. Wolisz, "A Perceptual Quality Model Intended Adaptive VoIP Applications", Special Issue Performance Evaluation of Wireless Networks and Communications of the Computer Communications Journal, Elsevier, May 2005, to be published.
[2] S. Möller, “The E-Model: A Analysis of the Source and Comparison with Published and New Test Results”, ITU Study Group 12 – Contribution 37, Dec. 1997.
[3] C. Hoene, S. Wiethölter, and A. Wolisz, "Predicting the Perceptual Service Quality Using a Trace of VoIP Packets", In Proc. of Fifth International Workshop on Quality of future Internet Services (QofIS'04), Barcelona, Spain, Sep. 2004.

## Slide 11: 2. Myth
A VoIP call must have toll quality!

## Slide 12: What is Toll Quality?
“Toll quality is the term normally given to commercially available voice services.”
How to measure it?
MOS (Mean Opinion Score)
  Systematic evaluation of call quality by human evaluators.
  Anything above good=4.0 is considered toll quality.
Using the ITU‘s planning tool „E-Model“
  R-factor >70 is considered toll quality.
  Depending on situation an advantage factor has to be considered.

## Slide 13: The Term Toll Quality is Arbitrary!
Every provider has a different call quality
  Some are good (and expensive)
  Others are bad (and often cheap)
Quality requirements depend on context
  In some situations users are willing or are expecting a different level of quality provision.
  E.g. on cellular phones or satellite phones [4].

## Slide 14: Result
Adapt call quality to requirements!
  Make it is as good as possible, or
  Make it better and charge more money.
  Make it better to win more customers [5].
References
[4] ITU-T Recommendation G.107, “The E-model, a computational model for use in transmission planning Recommendation G.107”, Mar. 2005.
[5] J. Holub, J.G. Beerends, R. Šmíd, ”A Dependence between Average Call Duration and Voice Transmission Quality: Measurement and Applications”, Proceedings of the Wireless Telecommunications Symposium 2004, May 2004.

## Slide 15: 3. Myth
If the quality gets worse, reduce the speech coding rate!

## Slide 16: Trade-offs
Coding rate
  Adaptive Multi-Rate (AMR) supports a coding rate from 4.75 to 12.2 kbit/s.
Packet Rate or Packetization
  AMR produces a speech frame every 20ms.
  One or multiple speech frames are packed into one VoIP packet
Drawbacks
  A lower coding rate decreases speech quality.
  A lower packet rate increases delay.

## Slide 17: Limited Bandwidth on an Ethernet-Link [1]

## Slide 18: Limited Bandwidth on IEEE 802.11b

## Slide 19: Results
If the wireless link is congested, a Wi-Fi VoIP phone shall adapt
  Packet rate
  Not coding rate!
  (only if already a low-rate coding is already applied.)
Why?
  Because every VoIP packet has a large overhead
    due to packet headers (e.g. IEEE, LLC, IP, UDP, RTP)
    due to MAC overhead (e.g. contention and collisions)

## Slide 20: 4. Myth
Two codecs are enough!

## Slide 21: Heterogeneous End Terminals
VoIP phones are used for all kind of calls
  to other VoIP phones
  to analogue phone
  to ISDN phones using G.711 coding
  to DECT telephones using G.726 coding
  to GSM telephones using GSM, GSM-FR, GSM-HR
  to UMTS phones using AMR coding
  …
VoIP phones call others phones
  directly over an IP-backbone (fine!)
  via a PSTN gateway (fine?)

## Slide 22: Tandem-Coding
PSTN gateways convert
  Signaling (from SIP or H.323 to SS7).
  VoIP speech flows to PSTN connections.
  Transcoding of speech signal.
Multiple codecs in row are called
  Tandem-Coding
  Transcoding
Tandem-Coding
  Decreases speech quality significant.
  Increases latency (because of algorithmic delays)

## Slide 23: Solution
Use one codec end-to-end !
No problem if VoIP on both ends,
otherwise
  IP phone shall support codec of other PSTN phone.
  e.g. G.711, G.726, GSM, AMR, …
  Gateways shall be transcoding-free.
Thus, IP phones shall support codecs of all common PSTN phones.

## Slide 24: 5. Myth
Telephony is narrow-band speech.

## Slide 25: Old days
PSTN is narrow-band (NB)
  8 kbit/s sampling rate
  3.6 kbit/s frequency band
  Using input filters
No reasons for VoIP to stick to NB.
Is wide-band (double bandwidth) better?
No reasons for VoIP to stick to WB.

## Slide 26: High Fidelity Wi-Fi Voice
Use full bandwidth of human hearing!
  CD Quality (stereo or 5.1)
Connect HiFi systems and sell it to teenagers!
  They pay also a lot for ring tones.
Allow musician to play together on phone!
  Requires low latency.
Narrow-band is like black-and-white TV.
  It will die soon!
Challenges: Latency, synchronization, codecs.

## Slide 27: 6. Myth
The packet loss rate relates
to speech quality.

## Slide 28: Introduction
Losing one Voice-Over-IP frame impairs the perceptual quality in a wide range [6], depending on
  the frame speech properties
  the encoder/decoder/concealment algorithms
  decoders resynchronization time after loss (especially low-rate decoders might maintain a wrong state after loss for the following frames.)
  the surrounding speech.
Example: Discontinuous Transmission (DTX)
  Speech frames during silence are less important
  Lower frame rate during silence

## Slide 29: Measuring the Importance of a VoIP frame
Using PESQ to measure the loss of one speech frame
Speech frames differ largely
Mean Importance [MOS*s]

## Slide 30: PESQ not verified  conduct listening tests
Can PESQ measure frame importances? Nobody knows…
Thus: Conduct formal listening-only tests! [7]
Problem: Humans cannot hear single frame losses!
Human just can hear multiple frame losses.
Thus, drop multiple similar frames…
PESQ can identify similar frames.

## Slide 31: Just try it: www.tkn.tu-berlin.de/research/mongolia

## Slide 36: Human LQS-MOS vs. PESQ LQO-MOS

## Slide 37: Speech Frames – Dropping Strategy [8]
Lost packets in cases of
Congestion
Wireless fading
Saving energy
Best: dropping the unimportant frames first
Worst: dropping the important frames first
Random frames losses
DTX: drop first silent frames, then active frames (randomly)

## Slide 38
Best
DTX

## Slide 39: Results
Speech frames and VoIP differ greatly.
If packets have to be dropped, drop unimportant packets first.
References
[6] C. Hoene, B. Rathke, and A. Wolisz, "On the Importance of a VoIP Packet", In Proc. of ISCA Tutorial and Research Workshop on th Auditory Quality of Systems, Herne, Germany, April 2003.
[7] C. Hoene and E. Dulamsuren-Lalla, "Predicting Performance of PESQ in Case of Single Frame Losses", In Proc. of MESAQIN 2004, Prague, CZ, June 2004.
[8] C. Hoene, S. Wiethölter, and A. Wolisz, "Calculation of Speech Quality by Aggregating the Impacts of Individual Frame Losses", In Proc. of Thirteenth International Workshop on Quality of Service (IWQoS 2005), Passau, Germany, June 2005.

## Slide 40: 7. Myth
The distance between two WLAN nodes
is measured best with
Received Signal Strength Indication (RSSI).

## Slide 41: Location Based Service
VoIP needs location based services for
  E911 calls.
  Cinema/theater/conference vibration alarm.
  Integrated value added services.
WLAN based LBS use
  GPS, outdoors.
  Received signal strength indication and triangulation to access points, indoors.
RSSI is imprecise and requires area maps.

## Slide 42: Measuring Round Trip Times

## Slide 43: Round Trip Time (RTT) and Distance
Problems:
Off-the-shelf WLAN cards: Resolution of 1 µs.
Does it really work?

## Slide 44: Experiments using IEEE 802.11b Prism II

## Slide 45: Experimental Results

## Slide 46: 2. Experiments: Using Latest Chip Sets.
Going outdoors with 802.11g and 802.11a.
Atheros and Prism GT (First is better).
RTT is better than RSSI!

## Slide 47: Time vs. Distance Precision

## Slide 48: Results
Without special hardware many RTT values are required.
With 1000 values you get nearly perfect accuracy.
You can measure it during an ongoing transmission.
Thus, not additional traffic is required.
During VoIP call an distance update every 50s.
References
[9] A. Günther and Ch. Hoene, "Measuring Round Trip Times to Determine the Distance between WLAN Nodes", In Proc. of Networking 2005, Waterloo, Canada, May 2005.

## Slide 49: Conclusion
Substantial reduction of energy consumption
if only important frames are transmitted.
Use RTT instead RSSI.
Perceptual quality models!
Email: hoene@ieee.org
WWW: http://www.tkn.tu-berlin.de/~hoene/